## Slide 1: Alberta Transportation Benefit-Cost Model
An introductory course
Bill Kenny, P.Eng
Lei Ma, P.Eng, M.Eng, PTOE, PMP
Rokibul Khan, P.Eng. M.Eng
November 22, 2018
1

## Slide 2: Course Outline
Module 1: Introduction
Module 2: Defining Your Project
Module 3: Defining Project Alternatives
Module 4: Breaking Down the Results
Module 5: Increasing Curve Radius
Module 6: Bridge Project
Module 7: Overlay vs Grade-Widening
Module 8: To Pave or Not to Pave
2
Notes: This course is divided into 7 Modules: Introduction, Defining Your Project, Defining Your Alternatives, Analysis, Results and Interpretation, and 3 examples.

## Slide 3
Module 1: Introduction
3

## Slide 4: Benefit cost (B/C) analysis
What is it?
4
Notes: What is benefit cost analysis?

## Slide 5
B/C analysis evaluates changes in benefits and costs over time arising from an investment in one of several alternatives, as compared to a ‘do minimum’ option.
It is an aid to judgment.
5
Notes: With regards to transportation project evaluation, benefit cost analysis measures the changes in benefits and costs over time arising from an investment in one of several alternatives, as compared to a ‘do minimum’ option.

## Slide 6
b/c analysis determines whether a proposed project is economically desirable
A standard indicator is if the IRR is equal to or greater than 4% at year 20 or at the end of the service life (whichever comes first).
6
Notes: A benefit cost analysis determines whether a proposed project is economically desirable (when benefits exceed costs). More specifically, in the context of Alberta Transportation projects, a project is considered cost-effective when the Internal Rate of Return* at year 20 or at the end of the service life of the improvement (whichever comes first) is 4% or greater. This is assuming all of the standard assumptions and costs are used as per the model. * The IRR is a defined term, see Excel or other references. Other measures may also be used to differentiate projects. BK.

## Slide 7: B/C analysis can also be used:
    To select the most beneficial alternative
    To compare the long-term economic effects of improvements that may accomplish different objectives
    To compare projects
    To compare programs
    based on economic
    conditions
7
Notes: Benefit cost analysis can also be used with other information to select which project among competing project alternatives should be funded given a budget constraint, to compare the effects of projects that may accomplish different objectives, to generally compare projects, and to compare programs based on economic conditions.

## Slide 8: What is B/C analysis NOT?
    A forecast of general economic consequences
    An economic model providing insight into the impact upon, change to, or relationship between prices, labor, interest rates, exchange rates, productivity, consumption or investment
    A substitute for good judgment
8
Notes:     Benefit cost analysis is not:
    1. A forecast of general economic consequences
    2. An economic model providing insight into the impact upon, change to, or relationship between prices, labor, interest rates, exchange rates, productivity, consumption or investment
    3. A substitute for good judgment

## Slide 9
Design Bulletin #86 – Benefit Cost Model and User Guide
AT Benefit Cost Model
  File Name: ATBenefitCostModelV2.xlsx
AT Benefit Cost Model User Guide
  File Name: ATBCMUserGuideV2.pdf
AT Documents
9
Notes: Design Bulletin #86 came out in the spring of 2015 and introduces the new departmental benefit cost model and user guide. The model has undergone a significant update – version 2 was released in February 2017.

## Slide 10
Model Overview

## Slide 11
To provide a method of comparison for various investments
Purpose
11
Notes: The purpose of the Alberta Transportation Benefit Cost Model is to provide a method of comparison for various investments. The exact purpose will vary depending on the nature of the investment under consideration and possibly depending on what it is being compared to. Sometimes B/C ratio, payback period, Internal Rate of Return or Net Present Value / Capital Cost or several of these will be useful. BK.

## Slide 12
  Construction costs
  Rehabilitation costs
  Operating & maintenance costs
  Road user costs
      Vehicle operating costs (2 options, all calibrated for Alberta using $0.505/ km)
      Travel time costs
      Collision costs
  Environmental costs
Analysis Components
12
Notes: The analysis components include: initial construction project costs (investment), rehab costs, operating and maintenance costs (can be scheduled and/or specified), road user costs (vehicle operating cost, travel time cost, collision cost), and environmental costs

## Slide 13
other cost types may be relevant
these can be defined in user-defined categories as a capital cost or on-going operating cost
Other costs
Notes: Note that other cost types may be relevant for some projects. For example, there may be costs associated with the protection of environmental assets, or costs associated with the mitigation of potential negative environmental impacts of a project. These costs can be defined in user-defined categories as a capital cost or on-going operating cost.

## Slide 14
Model Features

## Slide 15: Analysis of up to 3 alternatives (including a ‘do minimum’ alternative)
15
Notes: Analysis of up to 3 alternatives, including a ‘do minimum’ alternative. These Alternatives refer to different projects, or major variations on a project, that could be undertaken, which are compared to a ‘do minimum’ alternative, i.e. Alternative 1.

## Slide 16
  Up to
  80 year
  timeframe
16
Notes: Up to 80 year time frame for the analysis.

## Slide 17
  Flexibility in
  user-defined categories
17
Notes: Flexibility in user defined parameters, such as project definition, construction cost, construction period, operating and maintenance cost, and vehicle definition.

## Slide 18
Limitations of
the Model

## Slide 19
  Limited indicators
  For the ‘do minimum’ alternative (Alt 1)
19
Notes: There are limited benefit cost analysis indicators for Alternative 1 (the ‘do minimum’ alternative) as most indicators require the estimation of ‘benefits’ as the savings in costs determined by comparing the present value of costs for one alternative against Alternative 1. The benefit cost analysis indicators for Alternative 1 are discounted total cumulative costs and discounted investment costs.

## Slide 20
  Quality of the
  analysis results
  depends on quality of information
20
Notes: As with all models, the quality of the analysis and results will depend on the quality of information used to conduct the analysis. Garbage in, garbage out.

## Slide 21
  Limited to evaluating specific projects or programs
  and not the infrastructure system
21
Notes: The model is limited to evaluating individual projects or programs and not the infrastructure system. An example of “programs” would be a generic system wide, shoulder rumble strip program. BK

## Slide 22
  For bridge projects, the 80 yr time frame is limiting as bridge life is 100 yrs
22
Notes: For bridge projects, the 80 year time frame for analysis is limiting considering the expected life of a bridge is typically 100 years. According to bridge section, this is not a problem as they have a work-around by building in a residual value as needed. Also, once you get to 80 years the significance is very small as all future costs and benefits are discounted by multiplying by 1/ (1.04) to the power of 80 = 0.04338 BK

## Slide 23
Differences from MAE

## Slide 24
MAE is a tool that was developed based on similar decision making tools used in other jurisdictions.
It is intended to make decisions on a preferred option(s) at planning levels
      where there are significant differences between options,
      data and information are incomplete, and
      objectives are contradictory.
In contrast, at more detailed levels of planning and design, where options are close together and data and information are more reliable, BC Analysis is a more appropriate tool.
What is Multiple Account Evaluation (MAE)?
24
Notes: The analysis components include: initial construction project costs (investment), rehab costs, operating and maintenance costs (can be scheduled and/or specified), road user costs (vehicle operating cost, travel time cost, collision cost), and environmental costs

## Slide 25
  Levels of Transportation Planning
25
Network/System
Conceptual
Functional
Operational
Decreasing Range of Options, increasing level of detail/accuracy
Decisions based on strategic policy
Decisions based on procedural policy
Notes: As with all models, the quality of the analysis and results will depend on the quality of information used to conduct the analysis.

## Slide 26
Model Outline –
Four Main Components
General Inputs
Defining the Project
Analysis Results
Analysis Support Data

## Slide 27
Parameters tab
Analysis definitions
Project type categories
Various cost categories
27
Notes: The general Parameters tab contains default information, including analysis definition factors, project type categories, and various cost categories. Some of these variables can be altered for specific analyses (in the Project Definition tab) where the default values are not appropriate.
It should be stressed that if the user is at all uncertain about the accuracy of any values they may wish to input, the default values should always be used. When there is project specific information, project specific values should typically be entered rather than changing the defaults. An example of where modifying the default values themselves (in the Parameters tab) might be helpful is if the user is working on a large project with many alternatives, where the spreadsheet is being duplicated several times – this would save the user from having to re-enter the same project-specific information every time.

## Slide 28
Maintenance tab
Maintenance costs for each of the three Scheduled maintenance categories & calculates costs for each segment
28
Notes: Maintenance tab provides the maintenance costs for each of the three Scheduled Maintenance categories and calculates the associated costs for each segment of the project alternative.

## Slide 29
Calculates road user costs associated with vehicle running costs, travel time costs and emission costs.
RUC Alt# (3 tabs)
29
Notes: The Road User Cost (RUC) Alt tab calculates the road user costs (per day) associated with vehicle running costs, travel time costs and emission costs. These costs are estimated by vehicle type for each segment of the project defined by the user in the Project Definition area. A separate tab exists for each Alternative (up to 3).

## Slide 30: Collision Rates tab
Local data
30
Notes: The collision rates tab provides Alberta data for collision rates on various road types. If project specific values are not available, these charts may be consulted to provide a representative value. If the charts are not applicable to your project (e.g. you’re evaluating a gravel road), the default values may be used.

## Slide 31
Emissions tab
emissions rate (gms/km) by the speed of vehicle for each vehicle type and for each defined emission type
31
Notes: Emissions tab provides the rate of emissions in grams per kilometre for each vehicle type and for each emission type defined by the user in Parameters. Note – if the vehicle types and/or emission types are re-defined, the emissions will need to be updated to reflect the new categories defined by the user.

## Slide 32
Fuel Consumption tab
The Fuel & Non-Fuel (California) approach to estimating vehicle operating costs requires an estimation of fuel consumption by speed and vehicle type.
32
Notes: The Fuel & Non-Fuel (California) approach to estimating vehicle operating costs, which will be explained in more detail later, requires an estimation of fuel consumption by speed and vehicle type. This tab provides the fuel consumption speed adjustment factors for various vehicle types.

## Slide 33
B. Defining the Project

## Slide 34
Ex. defining ‘Increasing Curve’ project
Alt 1
Alt 2
Alt 3
34
Notes: The following slides will show how the “Increasing Curve” project is defined. We will go over this example in greater detail, including analysis of results, later on.

## Slide 35
Project Defn tab
Contains information specific to the project being analyzed
35
Notes: The general Project Definition tab contains information specific to the project being analyzed. This includes selecting your method of calculating vehicle operating cost, identifying your project name, the labels that will be used for the model, and possible changes to default values (set in the Parameters tab) by entering project specific values.

## Slide 36
Alt # (3 tabs)
Information specific to Alternative being analyzed.
Requires inputs about each Alternative.
36
Notes: Alt tabs contain information specific to the Alternative being analyzed. Requires inputs about each Alternative.
Alt 1 should be the ‘do minimum’ option against which other Alternatives are evaluated.

## Slide 37
TrafficAlt # (3 tabs)
Projects traffic for each Alternative and applies this forecast to the unit costs for vehicle operations, travel time, emissions and collisions.
37
Notes: Calculates the traffic projected for each Alternative and applies this forecast to the unit costs for vehicle operations, travel time, emissions and collisions.

## Slide 38
C. Analysis Results

## Slide 39
Project Costs Alt # (3 tabs)
Summarizes costs associated with each Alternative
Requires manual input of rehabilitation costs
39
Notes: Summarizes the costs associated with each Alternative defined by the user over the analysis timeframe. Also requires the user to manually input the rehabilitation and reinvestment costs (in present values) over the analysis period based on the anticipated future work.

## Slide 40
Results tab
Detailed benefit-cost analysis results for each year and each Alternative
40
Notes: Calculates the detailed benefit-cost analysis results for each year and each of the Alternatives defined by the user.

## Slide 41
Summary tab
Summary of the benefit-cost analysis results for each Alternative
41
Notes: Provides a summary of the benefit-cost analysis results, comparing the economic feasibility of all of the Alternatives to one another.

## Slide 42
D. Analysis Support Data – Located in a Separate File

## Slide 43
Emissions Conversion Table
Takes the CalTrans Benefit Cost model’s vehicle emissions estimates (as input by the user) and converts to metric.
This data is imported into the Emissions tab.
43
Notes: Takes the CalTrans Benefit Cost model’s vehicle emissions estimates (as input by the user) and converts the imperial measures for speed and volume to metric. This data is imported into the Emissions tab in the model.

## Slide 44
Value Updates Table
Uses historical cost indices to update various values used in the model
44
Notes: This spreadsheet uses historical cost indices to update various values used in the model.

## Slide 45
Important
Information

## Slide 46
Getting Started
A 20-Steps Cheat Sheet has been included into the model.
The user can follow these steps to complete the analysis.
There are two versions of Model: one is password protected, one is not password protected.
Usually, the user should use the password protected version to complete the analysis.
The user may update the unprotected version to suit for the specific project. Permission from AT is required if user wants to complete the submission with unprotected version.
46
Notes: As this model does not include inflation, the discount rate used to account for the time value of money, and bring all future dollar values back to the base year, must be a ‘real’ discount rate.

## Slide 47
Real Dollars
This model deals with all values expressed in real base year dollars and does not include inflation.
All base values and expenditure data need to be expressed in these terms.
47
Notes: This model deals with all values expressed in real base year dollars, i.e. present estimated values, and do not include inflation. As a result, all base values and expenditure data used in the model will need to be expressed in these terms.

## Slide 48
Real Discount Rate
As this model does not include inflation, the discount rate used to account for the time value of money must be a ‘real’ discount rate.
Alberta Government recommends using an annual discount rate of 4% for all future costs and benefits.
48
Notes: As this model does not include inflation, the discount rate used to account for the time value of money, and bring all future dollar values back to the base year, must be a ‘real’ discount rate.

## Slide 49
Perspective
The components of b/c analysis and their valuation depends upon the perspective defined for the analysis.
For this model, the perspective is the social point of view for the Province of Alberta.
49
Notes: The components of a benefit cost analysis and the valuation of these components depends upon the perspective defined for the analysis. For this model, the perspective is the social point of view for the Province of Alberta. This social perspective should consider all relevant expenditures and costs for society’s point of view, limited to Alberta.

## Slide 50
Inputted Values – Shadow Prices
Sometimes the market does not provide values for relevant components, or market value does not reflect their ‘social’ value from the defined perspective.
Where this is relevant, adjustments may be required.
e.g. travel time has no ‘market’ value, but has a ‘social’ value
50
Notes: In some cases the market does not provide values for some components relevant in this analysis, or the market value does not reflect the ‘social’ value of these components from defined perspective. As a result, where this is relevant, there may need to be adjustments to the values used in the analysis. In other instances, where these values are not available from market information, imputed values or shadow prices should be considered.
For example, the travel time associated with passengers has no ‘market’ value. However, studies have been conducted into the ‘social’ value of travel time for passengers. The most relevant of these estimates should be used in the analysis to quantify this component.

## Slide 51: A Buck is a Buck
The model provides default values for items that are difficult to monetize.
Dollars expended or saved (in the same year) are of equal value regardless of source or beneficiary.
Weightings should not be applied to dollars.
Users can over-ride the defaults but this is considered “exceptional” and should be justified in writing.

## Slide 52
Transfers
Some types of revenue and expenditures, from a social perspective, do not represent real change, but are rather transfers from one group of economic agents to others.
e.g. subsidies*, grants* and taxes*
*These are removed from the analysis.
52
Notes: Some types of revenue and expenditures, from a social perspective, do not represent real change, but are rather transfers from one group of economic agents in the economy to others. e.g. subsidies, grants and taxes – all of these are transfers from taxpayers to other groups in the economy.

## Slide 53
Direct Expenditures & Costs
New economic activities not only contribute to economic growth, but also create potential for additional expenditures on indirect and induced economic activities.
In this model, only direct expenditures and costs have been included.
53
Notes: New economic activities, such as construction, not only contribute to the growth of the economy, but also create the potential for additional expenditures on indirect and induced economic activities. These additional indirect and induced expenditures are associated with upstream purchases of goods and supplies required to support the project and the subsequent income effects generated by the project. In this model, only the direct expenditures and costs have been included in the analysis.

## Slide 54
Terminology

## Slide 55: Net Present Value
NPV measures the net benefit of a project in today’s dollars: the sum of all benefits minus the sum of all costs.
All values are discounted to the current year using the standard discount rate (4% per annum).
55
Notes: Measures the net benefit of a project in today’s dollar terms. Money has a time value, known as an opportunity cost, which means that money invested today could earn interest elsewhere. To compensate, future payments need to be higher so that they equal today’s dollars. Additionally, time value accounts for the cost of capital, investment money that costs the company to borrow over time at a specific interest rate.

## Slide 56
NPV in this analysis
compares the net cost savings
of one alternative
the ‘do minimum’
(alternative 1)
vs.
56
Notes: NPV in this analysis compares the net cost savings of one alternative against the ‘do minimum alternative’ which should be Alternative 1. This is necessary because all of the analysis information represents costs (e.g. there are no revenues as is typically the case in benefit/cost analysis of business alternatives). As a result, it is the net cost savings of one alternative against another that is relevant.

## Slide 57: Benefits
Cost savings (if any) compared to Alternative 1
Numerator for the benefit cost ratio
57
Notes: Benefits of an alternative are the cost savings (if any) as compared to Alternative 1. This is the numerator for the Benefit Cost Ratio.

## Slide 58: Investment costs
construction costs
denominator for the benefit cost ratio
associated rehab costs
58
Notes: Investment costs include construction costs plus any associated rehabilitation costs. Investment costs for a given alternative are compared to Alternative 1 so they can be used as the denominator for the Benefit Cost Ratio.

## Slide 59: Benefit Cost Ratio
present value of benefits
present value of investment and other costs
59
Notes: The Benefit Cost Ratio is equal to the Benefits (non-Construction Cost / Rehabilitation Cost) or cost savings of the selected alternative as compared to the difference in cost between the selected Alternative and Alternative 1.
One can also take the net present value divided by the costs as an indicator of the relative benefit compared to overall costs.

## Slide 60: Internal rate of return (IRR)
the rate of discount that makes the net present value of the benefits minus the net present value of costs equal to zero
60
Notes: Internal Rate of Return, of IRR, is the discount rate that makes the net present value of all cash flows from a particular project equal to zero. The IRR on the investment in one alternative is compared to Alternative 1.

## Slide 61: Payback period
the period of time required to recoup the funds expended in an investment, or to reach the break-even point.
61
Notes: Payback Period: the number of years that it takes to recover the costs in one alternative compared to Alternative 1.

## Slide 62: NPV/ Cost
Net present value
present value of investment costs
62
Notes: The NPV / Cost is equal to the Net Present Value of all Benefits minus Costs divided by the present value of investment costs..
One can also take the net present value divided by the costs as an indicator of the relative benefit compared to overall costs.

## Slide 63: Sunk costs
Expenditures that have occurred in the past and are not recoverable.
They are not relevant.
63
Notes: Sunk costs, or expenditures that will have occurred in the past and are not recoverable, are not relevant for consideration in benefit-cost analysis. Benefit-cost analysis is forward looking with the aim of providing information about future investment decisions.

## Slide 64: Questions?
64