## Slide 1
Module 2: Defining your Projects

## Slide 2: Note:
Orange cell = input cell
Drop-down list looks like:
Notes: The model has been designed so that all user inputs are entered in cells with an orange background, as shown in this slide. In some instances, a drop down menu has been built into the model with pre-defined selections for the user to choose from. To get the drop down menu, click in the cell and the selection options will become visible. In this case, the California Road User Cost has been selected by the user from the drop down list and is shown in the selection after the user hits ‘return’. As we will explain later, the California method is the preferred method to be used to calculate road user costs.

## Slide 3: Entered information
user input cells
entered elsewhere
Notes: Information that has been entered in the model and used elsewhere in the model is displayed as orange text in either a white or grey background as shown. In this example, each of the vehicle types (e.g. Passenger, RV, etc.) have been entered by the user elsewhere in the model and are shown here in orange text. Similarly, the default values for Occupancy, WorkBus $/hr and Other $/hr were entered elsewhere.
In many cases, the default values may be modified when data is available at a Project level. However, the changes to default values should typically only be made in the project specific value user input cells (as indicated in the screenshot).

## Slide 4: Collision Rates
All cells that do not allow input from the user have been ‘locked’ and ‘protected’
Notes: All cells that do not require an input from the user have been ‘locked’ and ‘protected.’ This will ensure that these cells are not accidentally altered. Altering cells that do not require information from the user may affect the integrity of the model’s calculations.

## Slide 5: Preparing for analysis
Every analysis will require the development of information for a ‘do minimum’ (Alternative 1) option and at least one (up to two) Alternatives.
Notes: Before working with the model, it may be valuable to review the required information so it can be collected and/or generated prior to starting the analysis. Every analysis will require the development of information for a ‘do minimum’ (Alternative 1) option and at least one (up to two) Alternatives. The same information will be required for each of these Alternatives.

## Slide 6: Step one
Decide which analysis method to use for vehicle operating costs.
Notes: Decide which analysis method to use for vehicle operating costs.

## Slide 7
Vehicle operating costs: 2 approaches
Notes: The model contains two approaches to estimate vehicle operating costs.

## Slide 8: Preferred: California (Fuel & Non-Fuel Cost) Approach
      Based on the California Department of Transportation’s (Caltrans) benefit-cost model
      Used when curvature/gradient does not vary significantly between alternatives
Notes:       The first and preferred method is the California approach (also referred to as the Fuel & Non-Fuel approach). The California vehicle operating costs are estimated using fuel and non-fuel vehicle operating costs for each vehicle type based on the segment length and running speed, not considering the effect of gradient or curvature specified in the model. It is based on the California Department of Transportation’s (Caltrans) benefit-cost model.

## Slide 9: Texas (Curvature & Gradient) approach
  Uses road operating costs based on the Department’s 1991 benefit cost model
  Used only when curvature and/or gradient varies significantly between alternatives
Notes:       The Curvature & Gradient (Texas) method uses factors that originated in part from data compiled by the Texas Research and Development Foundation in 1982 for the Federal Highway Administration. For the Department’s original b/c model, these numbers were converted to 1988 dollars and updated to 2012 based on the Transportation Price Index. For more details refer to the AT Benefit Cost Model Guide.

## Slide 10
In the project definition tab, select method of calculating vehicle operating costs.
Notes: In the project definition tab, select your method of calculating vehicle operating costs.

## Slide 11: Name your project
Notes: The project being evaluated should be labeled by entering a Project Name.

## Slide 12: Project definition table
An overview of the alternatives’ names
Notes: This table provides an overview of the Alternatives’ names. Up to 3 alternatives can be defined for each project being evaluated. The names are defined in the Alt # tabs.

## Slide 13: Construction start/end year table
Notes: This table provides an overview of the Alternatives’ construction start and end dates, and when the project would begin operations. The timing of construction is defined in the Alt# tabs.

## Slide 14: Decide on
OR
Project Specific Values (PSV’s)
Defaults
Notes:       Decide whether you would like to use project-specific values (psv), or the defaults in the model.

## Slide 15: Project-specific values
Vehicle Occupancy
Unit Cost of Time – Travel for Business
Unit Cost of Time – Travel for Other
Non-Fuel Vehicle Cost per km
Fuel Cost per Litre
Fuel Taxes per Litre
Fuel Efficiency (Litre/100 km)
Notes: Project specific values can be entered for all of the items shown on this slide. If uncertain about the accuracy of your information, it is better to use defaults provided in the model.

## Slide 16: Vehicle occupancy and time costs
Notes: These are the default values for vehicle occupancy and time costs. The 7 default vehicle types are shown here, but up to 10 vehicle types can be entered (in the Parameters tab).

## Slide 17: If there are PSV’s, enter them here
Notes: If there are project specific values, enter them in the orange cells.

## Slide 18: If PSV’s are entered, they will be used throughout the model.
Notes: If project specific values are entered, those values will be used throughout the model; otherwise, leave empty to use defaults.

## Slide 19: Fuel and non-fuel vehicle operating costs
Notes: These are the default values for vehicle operating costs used for the California/Fuel&Non-fuel approach to estimating vehicle operating costs (from the Parameters tab). The tax has been removed from the calculation as it is not a societal cost.

## Slide 20: The aforementioned can be adjusted in Parameters tab.
Notes: These default values may be modified in the Parameters tab as shown on this slide. However, they would typically not be modified – rather, the user would just enter their values as a project-specific value.
An example of when the values under the Parameters tab might be modified is if the user is evaluating a large project with multiple alternatives, which likely would involve making duplicate copies of the spreadsheet – having their own values input as the defaults would save them time and would help avoid any accidental mistakes (e.g. forgetting to change a value in one alternative but not another).

## Slide 21: If there are PSV’s, enter them here.
Notes: The default values for vehicle operating costs used for the California/Fuel&Non-Fuel approach (from the Parameters tab) can be modified for the project by entering the desired value in the project specific values field (orange cells).

## Slide 22: If PSV’s are entered, they will be used throughout the model.
Notes: If project specific values are entered, those values will be used throughout the model; otherwise, leave empty to use defaults.

## Slide 23: Questions?
23