## Slide 1
Module 3: Defining your Alternatives

## Slide 2: Preparing for
Notes: Every analysis will require the development of information for a ‘do minimum’ option and at least one (up to two) Alternative options.

## Slide 3
Consider Alternative 1 as the ‘do minimum’ alternative, Then define the other alternatives to be analyzed.
Notes: The Alternatives to be evaluated are defined in the Alt # tab (i.e. Alt 1, Alt 2, Alt 3). To conduct an analysis, at least 2 Alternatives must be defined. It is important that Alt 1 be the ‘Do Minimum’ alternative against which other alternatives are evaluated. The determination of Benefits (or Cost Savings) are based on a comparison of the Non-Investment cost savings of each alternative against Alternative 1.

## Slide 4: Defining each alternative
  Project Type, selecting rural or urban setting
  Alternative Name
  Construction Start/End Year
  Original/Historic Project Cost (if applicable)
  Construction Cost
  Specified Operating and Maintenance Costs (if applicable)
  Collision Rates and Costs
  Project Segment Definition
  Intersection Definition (if applicable)
  Traffic Mix and Trip Purpose by Vehicle Type
Notes: This is the required information for the definition of each alternative. We will go over each in more detail.

## Slide 5
Project type
Don’t forget to select rural or urban!
Parameters tab
Notes: Select an option from the list of project type categories. The project type will have a default project life associated with it, which is meant to assist the user with determining when replacement costs would apply (which are input in rehab costs column in the ProjectCostsAlt# tabs). The project type categories (up to 20) can be modified in the Parameters tab.
The project should also be given a locale – either rural or urban.

## Slide 6
Alternative name
Notes: Enter a name that reflects an identifiable characteristic of the Alternative. As mentioned previously, Alternative 1 is meant to be the ‘Do Minimum’ Alternative.

## Slide 7
Operation will be the year following specified end year of construction
Construction start/end years
Notes: Define the years over which construction of the Alternative will take place. The year following the end of the construction period is assumed to be the first year of operation. Since there is no construction associated with this alternative, the start/end years of construction are the same.

## Slide 8
Original (historic) project cost
Notes: Defining the original (historical) cost of the project is optional if available, and would typically only be entered when no significant construction costs are needed for the alternative being examined. It is meant to be an informational reference value.

## Slide 9
Categories are defined in Parameters tab
Construction cost
Notes: The construction cost categories (which are defined in the Parameters tab) and construction period will define the cells that are available to enter the associated construction costs (orange cells). The total cost by category is provided in each column and total cost by year in each row.

## Slide 10: Operating & maintenance costs
Specified
Scheduled
Defined by user
From AT’s RODA model
Can use either, or a combination of both
Notes: Two approaches to determining operating and maintenance costs: Specified, which are defined by the user, and Scheduled, which are from Alberta Transportation’s RODA model. It is up to the user whether they want to use either one or a combination of the two.

## Slide 11
Operating & maintenance costs - specified
Notes: The user Specified O&M cost categories are used to enter the associated costs (orange cells). The total O&M costs for the first year of operation are totaled in the year 1 row. The O&M costs will increase according to the traffic growth rate, which is defined in the project segment definition section further down in the tab.

## Slide 12: Important
Entering Specified O&M costs will add them to Scheduled O&M costs identified in each segment.
If you wish to only use Scheduled O&M costs, enter a zero in each of the Specified O&M cost categories.
0
0
Notes: Important: any entered Specified O&M costs will be added to Scheduled O&M costs identified by segment as discussed next. Should the user wish to not use one or all of these categories, enter a zero in the relevant cell(s) (or ensure it is blank).

## Slide 13: Collision rates
Notes: Default Collision rates for rural and urban settings. The default values can be modified by entering the desired values in the Project Specific Values field. It was based on 2008-2012 data.

## Slide 14: Collision rates cont.
If project specific collision rates are available, they should be entered into the appropriate project specific values cells
Notes: If collision rates specific to the project location are available, they should be entered as project specific values in the corresponding cells.

## Slide 15: Collision rates tab (AT’s data) (if PSV’s are not available)
example:
Notes: Default Collision rates for rural and urban settings. The default values can be modified by entering the desired values in the Project Specific Values field. It was based on 2008-2012 data.

## Slide 16: Collision costs
Notes: Default values for collision costs. These were calculated by AT’s Office of Traffic Safety using Alberta data based on a willingness-to-pay model established by Transport Canada. For further details see references in the Guide.

## Slide 17: Project segment definition
Segment name
Length (km)
Surface type
Road type
Gradient
Traffic direction
Curvature radius
Curvature superelevation
Notes: The project segment definition is required to calculate various components of road user costs, as listed below. Input name for the segment and its length. Surface type should be either paved or gravel.
Road type can be either 2-lane, 4-lane undivided, 4-lane divided at grade or not at grade, or 6+lanes.
Gradient should reflect the best average for the segment (an integer from -8 to +8).
Traffic Direction – either one or two way.
For both curvature radius and superelevation, the best average for the segment should be selected. If these parameters start to vary significantly, consider separating the segment into two (or more) segments.

## Slide 18: Project segment definition cont.
Base year traffic (AADT)
Traffic growth driver type
Traffic growth rate
Default running speed
Average running speed
Scheduled maintenance cost category
Age of surface
Notes: Input traffic volumes for base year (AADT).
Traffic Growth Driver Type – can be either linear or exponential.
Identify traffic growth rate (which is set at 3% by default) and average running speed (note – this cannot be greater than 120 km/h as emissions table does not go higher). The default running speed is associated with a Project Type and can be changed in the Parameters tab.
Scheduled Maintenance Cost Category – select appropriate road maintenance cost category (e.g. Gravel, Paved Base, Paved 2nd) This will use the applicable costs in AT’s RODA model.
Age of surface – when using the scheduled road maintenance costs from the RODA model, it is necessary to specify the age of the surface.

## Slide 19
obtained from Parameters tab
Dropdown box cannot be deleted
Notes: Before entering data into this table, depending on the complexity of the project being analyzed, it may be necessary to plan how the inputs are best defined. While there are 20 possible segments that can be defined, for very complex projects it may be necessary to combine components that have common features, or make separate spreadsheets.
You’ll noticed the only value you can’t change in the Project Segment Definition tab is the Default Running Speed. This has been pre-defined in the Parameters tab, but can be modified there. However, it doesn’t make any impact on the results (the user-defined average running speed does) – it is just a guidance value.

## Slide 20: Important
Scheduled O&M costs will be added to Specified O&M costs indicated previously, unless ‘Do Not Use’ is selected.
Notes: Scheduled O&M costs must be selected for each segment to be used in the analysis. If you wish to not use the scheduled O&M costs (using only specified instead), then “Do Not Use” must be selected in each cell for each applicable segment.

## Slide 21: Intersection definition
Volumes and delays on approaches are converted into time loss costs based on time values for money.
Applicable to Project Type: Intersection (New or Upgrade) only.
Notes: When comparing intersection improvements, the user should enter estimated delay times (from capacity analysis software) in seconds per vehicle for AM Peak, PM Peak, and Off-Peak averages (both daytime and nighttime). Volumes on each approach must also be entered. These volumes and delays are converted into time loss costs based on the time values for money embedded in the model. The time loss costs are reflected in the TrafficAlt# tabs for each alternative.
This is only applicable to Project Type: Intersection (new or upgrade). When these project types are chosen, the time cost of travel will not be accounted in the road user costs – rather the time loss costs will instead.
Note: this method assumes that the growth rate of delay is equal to the traffic growth rate. Therefore, the user should ensure that the traffic growth rate is selected correctly under project segment definition.

## Slide 22: Project segment traffic mix
Must add up to 100 %
Notes: The mix of traffic must be allocated for each segment. The Traffic Mix must add up to 100% for each segment. If it doesn’t, an error message will appear.

## Slide 23: Trip purpose
Notes: The share of trip purpose (work/business or other) must be set for each Vehicle Type. When the share of trips that are Work/Business are entered for a Vehicle type, the share of Other trips is calculated automatically (that’s why it’s grey).

## Slide 24: Traffic Alt# (3 tabs)
No Inputs Required
For each segment, the tab calculates:
Notes: There are three traffic alt tabs, one for each alternative. No inputs are required in these tabs.

## Slide 25: Traffic Alt# (3 tabs) cont’
  Traffic forecast (AADT)
  Running costs for grade (if using Texas method)
  Running costs for curvature (if using Texas method)
  Travel time costs
  Time loss costs – if Project Type is Intersection
  Collision costs
  Emission costs
  Vehicle operating costs (if using California method)
No inputs required
Notes: These tabs do not require any user inputs; they provide a detailed breakdown of the traffic forecast (growth rate is specified in definition of alternative), running costs for grade and curvature (if using Texas method), travel time costs, collision costs, emission costs, and vehicle operating costs (if using California method). If the Project Type is selected as Intersection – New or Upgrade, then time loss costs will populate instead of travel time costs. All costs listed are per day.

## Slide 26: Questions?
26