## Slide 1
Module 4: Breaking Down the Results
1

## Slide 2
Costs for each alternative are summarized in these categories:
        Construction
        Operating and Maintenance
        Road User
        Emission
Rehab costs must be entered manually over the analysis period for each alternative
Project Costs Alt# (3 tabs)
2
Notes: The costs for each Alternative defined for the project are summarized in the Project Costs Alt # tabs. The costs are provided over the 80 year forecast period for each of the major project cost categories, i.e. the following: construction costs, operating and maintenance costs, road user costs, and emission costs. These costs are then summed to provide a total for each year. Note: rehab costs MUST be entered manually over the analysis period for each alternative in their present estimated values. If they are not entered, the model’s results will be skewed from reality.

## Slide 3: Project cost graphs
Investment costs
Other costs
&
3
Notes: For each alternative two graphs of cost are provided. These charts are at the bottom of each corresponding ProjectAlt tab. They are labeled Alt1Invest, Alt1Other, Alt2Invest, etc.

## Slide 4: Alt# investment costs graph
Infrastructure costs
Life cycle & reinvestment costs
4
Notes: Investment costs include infrastructure costs and related life cycle / rehabilitation costs over the forecast period. Here, since Alternative 1 was the “do minimum” alternative, there was no capital investment associated with it and thus there is no blue on the graph.

## Slide 5: Alt# other costs graph
5
Notes: The “Other costs” graph includes all the other costs associated with the selected Alternative, including travel time, time delay (if applicable) collisions, emissions, maintenance (scheduled and specified), and vehicle operating costs. Note that only the selected method for vehicle operating costs will show on the graph. In this example, Texas method has been selected, which is why the bottom majority of the bars are purple. Clearly vehicle operating costs make up a large portion of the other costs, followed by travel time, collision, and emissions (in descending order for this case). Maintenance costs are almost negligible in comparison.

## Slide 6: Construction costs table
6
Notes: The construction costs will take whichever values were specified in the Alt # tab for all the various construction cost categories. As a reminder, up to 8 different construction cost categories can be entered (this can be done in the Parameters tab). Historical capital investment is not included in the total construction costs, regardless if a value is input or not. Rehabilitation costs must be entered manually for each alternative based on the expected work and estimated life of the asset at their present estimated values.

## Slide 7: Operating & maintenance costs table
7
Notes: The operating and maintenance costs are broken down as in the screenshot shown. If specified maintenance values have been inputted (Alt # tab), then they will be shown here. In this case, only scheduled maintenance has been indicated. The scheduled maintenance is calculated in the maintenance tab for each segment and then added together. 3 segments have been specified for this example, so their respective totals have been summed to obtained 6,285 in scheduled maintenance every year. The total project costs shown in the far right column is the sum of any construction costs and the O&M costs – for this example there were no construction costs as it was the “do minimum” alternative.

## Slide 8: Maintenance tab
Two options:
1. User defined specific to the project being evaluated
2. AT’s maintenance cost profile (RODA)
8
Notes: The AT Programming RODA O&M cost profile is shown in the screenshot for gravel, base pave, and second stage paving projects. If more applicable information is available, these values may be modified. The example shows the calculated maintenance costs for each specified segment based on the length, age of surface at the start of project (to determine the appropriate rehab cycle), and the type of maintenance category it has (all base pave).

## Slide 9: Road user costs table
9
Notes: The road user costs are broken down into vehicle operating costs, travel time costs, collision costs, and then totaled in the far right column. The type of analysis method for vehicle operating costs is shown at the top; in this case Texas has been chosen. Texas vehicle operating costs will add the costs for curvature and gradient calculated in the Traffic Alt tab and be multiplied by 365. California vehicle operating costs will take those calculated and calibrated in the Traffic Alt tab and multiply by 365. Similarly, Travel Time costs and Collision costs have been previously calculated in the Traffic Alt tab; here they have just been multiplied by 365 for a yearly amount. Reminder that Time Delay costs will only appear if the Project Type is Intersection (New or Upgrade).

## Slide 10: Emission costs table
10
Notes: Then, emission costs are shown. These values are also those previously calculated in the Traffic Alt tab and subsequently multiplied by 365 to obtain a yearly value.

## Slide 11: Totals column
construction costs
O&M costs
RUC costs
emissions costs
11
Notes: Finally, we add that all together. Construction + O&M + road user + emission costs to obtain a grand total for each year of that project.

## Slide 12: Results tab
12
Notes: The detailed results of the benefit-cost analysis are summarized in the Results tab. This includes results for each Alternative (remember, up to 3). Each Alternative is compared to ‘do minimum alternative’ (Alternative 1). The main indicators of economic desirability are those outlined in the Summary tab. IRR and Break Even Point are also calculated in the Results tab.

## Slide 13: Summary tab
Internal rate of return
Break even point
Discounted total cumulative costs
Discounted investment costs
Discounted benefits
Net present value (NPV)
NPV/Cost Ratio
Benefit cost ratio
13
Notes: An overview of the benefit cost analysis results, shown by economic indicators, is provided in the Summary tab. These indicators include IRR, break even point, discounted total cumulative costs, discounted investment costs, discounted benefits (non-investment cost savings), net present value, and benefit cost ratio.

## Slide 16: Questions?
16