## Slide 1
Module 5: Increasing Curve Radius

## Slide 2
ALTERNATIVE | RADIUS | TANGENT LENGTH | CURVE LENGTH | GRADE | TOTAL LENGTH (Point A to B)
1 (CURRENT) | 600 | 1,100 | 942 | 3% | 1,100 x 2 + 942 = 3,142
2 | 900 | 800 | 1,414 | 3% | 800 x 2 + 1,414 = 3,014
3 | 1,200 | 500 | 1,885 | 3% | 500 x 2 + 1,885 = 2,885
Alternatives
Alt 3
Alt 1
Alt 2
Point B
Point A
Notes: The Increasing Curve Radius example will go over use of the model step-by-step. Alternative 1 depicts the current situation. Alternative 2 is a flatter curve, and Alternative 3 is the flattest curve. Specific geometrics are shown in the table.

## Slide 3: Which method should we use?
?
Texas
California
OR
Notes: Knowing what we know about the California and Texas methods of calculating vehicle operating costs, which method should we use for this example?

## Slide 4: Texas!
Considers the effect of changing grade and curve radius
Notes: The Texas method is more accurate to use for this project because it takes into account the user cost associated with increasing the radius of the curve….

## Slide 5: Whereas
The California method only takes the slight difference in length between both into account.
Alternative 1:
942 + 1100 + 1100 = 3,142 m or 3.1 km
Alternative 3:
1885 + 500 + 500 = 2,885 m or 2.9 km
257 m difference

## Slide 6: Project Information
2-lane, undivided 7.4m wide paved highway in rural setting
Posted and running speed is 100 km/h
The road cost $2,000,000 to build originally in 2001.
Alt 2 costs estimated at $3M for construction, $5M for land
Alt 3 costs estimated at $3M for construction, $6M for land
For Alternatives 2 and 3, engineering and land costs are incurred in 2018 and construction costs are incurred in 2019
Engineering costs are 10% of construction costs
AADT at year 0 (base year) is 2,000
Traffic growth rate is 3%, linearly
Notes: This slide shows the project information

## Slide 7: Define your project
1. Go to ProjectDefn tab.
2. Click in the Vehicle Running Cost to select method: California (Fuel & Non-Fuel Costs), which is default, or Texas (Curvature & Gradient).
Notes: Go to project definition tab to select the vehicle running/operating cost determination method. As previously discussed, since in this example we are primarily looking at the result of modifying the curvature, we would choose to use the Texas method.

## Slide 8
3. Enter a name for your project.
4. Observe the remainder of the tab. Do you have project specific values?
?
Notes: Observe the remainder of the Project Defn tab. Consider whether you have project-specific values available for vehicle occupancy, unit costs for time, and vehicle operating costs. For our class examples we will be using default values for these items in the project definition tab.

## Slide 9
5. Go to Alt 1 tab.
6. Select Project Type by clicking on the cell.
7. Select whether the setting is rural or urban.
Notes: Choose a name for Alternative 1. Identify the Construction Start/End Years. Reminder that the year of operation will be the first following the end year of construction.

## Slide 10
8. Choose a name for Alternative 1.
9. Identify the construction start/end years.
Notes: Choose a name for Alternative 1. Identify the Construction Start/End Years. Reminder that the year of operation will be the first following the end year of construction.

## Slide 11
10. Enter original (historical) project cost (optional).
11. Enter construction costs. For Alt 1, no construction is required.
Notes: Enter the Original (Historic) Project Cost. This is optional, and is only applicable if no significant amounts of construction costs are needed with this alternative. Example: for a “do minimum” alternative. It will not affect your end results. If a reasonably accurate historical capital investment value is not available, this cell may be left blank. In benefit cost analysis terms, any costs incurred prior to the analysis are considered to be ‘sunk costs’ and not relevant to the future investment decision making.
Enter the construction costs. For Alternative 1, no construction is required, so these cells will be left blank.

## Slide 12
.
12. Enter any Specified O&M Costs. Leave blank to only use Scheduled O&M costs
.
13. Enter PSV’s for collision rate and percentage of collision type, if available.
?
Notes: Enter any Specified Operating and Maintenance costs. Up to 5 Operating and Maintenance Costs may be entered by going into the Parameters tab. Leave blank to only use Scheduled O&M costs, which will be specified in the segment definition section. For this example, we will only use the Scheduled O&M costs.
Next, the user has the option of entering Project Specific Values for Collision rate, and percentage of collision type for 6 different road types.

## Slide 13
If PSV’s are not available, the user can check the graphs / table under the Collision Rates tab.
W=7.4m, AADT=2000,
Collision rate=134
Notes: Typically we would check the Collision Rates tab to see if there are any applicable graphs we can use. In this case, we get a collision rate of 134 for 2 lane paved 7.6m wide road.

## Slide 14: Alt 1 – Collision Modifications
Notes: We would input our collision rate of 134 as a project specific value into the appropriate section in Alt 1. We leave the collision costs as defaults.

## Slide 15
14. Define project segments.
Notes: Next, define project segments. For this example, 3 segments are used for each alternative: 1 for each tangent and 1 for the curved portion. The screenshots show what the columns would look like if you inputted all the information as specified above. Note that due to the age of the existing surface, we would use the “Paved 2nd” Scheduled Maintenance Cost Category, and input the age of the surface in the last column.

## Slide 16
15. Define project segment traffic mix.
16. Define trip purpose by vehicle type.
Notes: Enter the project segment traffic mix. The user can enter different compositions of traffic streams for each segment. For example, if the project split into 2 different roads where one road was a truck route, the segments would likely have somewhat different traffic mixes.
Reminder: the user may change / enter more vehicle types in the Parameters tab, up to a maximum of 10 vehicle types.
Lastly, enter the trip purpose by vehicle type. If the user enters or changes the vehicle types earlier, the trip purpose by vehicle type should also be changed as necessary.
Defaults will be used for this example so no change is needed.

## Slide 17: Assuming the following
Alt 1 overlay at years 3, 23, and then reconstruction at year 43
Alternatives 2 and 3 are both new construction
Overlay every 20 years at $300,000 / km including engineering cost
Overlay twice, then reconstruction must occur
Reconstruction costs $3,300,000 for Alt1, 2 & 3 including engineering cost
ENTER the rehab costs for alternatives 1, 2 and 3
Notes: Project segment definition for Alternative 2. All other values will be left as defaults.

## Slide 18
17. Go to ProjCostAlt1 tab.
18. Enter rehab costs under ProjectCostsAlt1 tab.
18
Notes: Note that since Alternative 1 is referring to the second overlay happening now, we estimate that grade-widening would be required at year 20 to keep the road in an useable condition. Then, overlay costs would be required for years 40 and 60, to ensure accurate costs are accounted for the entire analysis timeframe. Reminder that all costs are entered in today’s dollars.

## Slide 19
Repeat steps 1-18
for Alternative 2 & 3

## Slide 20: Alt 2
Notes: Screenshots of what Alt 2 would look like.

## Slide 21: CMFs for Alt 2 and Alt 3
v = 100kph = 62.14mph
Alt 2:
x1 = 600m = 1968.5ft
y2 = 900m = 2952.76ft
CMF2 = 0.887
Alt 3:
x1 = 600m = 1968.5ft
y3 = 1200m = 3937.01ft
CMF3 = 0.835
Source: CMF Clearinghouse www.cmfclearinghouse.org
Notes: As we know that the collision likelihood will decrease with a flatter curve, we can estimate what the reduction in expected collision rates might be using an applicable CMF. Shown is a CMF function for an increase in horizontal curve radius from x to y feet.
We will apply these bolded numbers to our definitions of collision rates for Alternatives 2 and 3.

## Slide 22: Alt 2 - Collision Modifications
CMF2 from Alt 1 to Alt 2 = 0.887
Apply CMF2 to default collision rate: 134*0.887 = 118.858
Insert modified collision rate as a PSV:
Notes: Other than the difference in costs and geometry, Alternatives 2 and 3 will also have reduced collision rates. This shows how we would apply the CMF to collision rate for Alternative 2 and enter it in as a project specific value of 118.858.
Again, leave the collision costs as defaults.

## Slide 23: Alt 2 – Project Segment Definition
Notes: Project segment definition for Alternative 2. All other values will be left as defaults.

## Slide 24: Rehab costs, Alt 2
Notes: Rehab costs for Alt 2: we enter in an overlay cost at years 20, 40, and a reconstruction cost at 60 years.

## Slide 25: Alt 3
Notes: Screenshots of what Alt 3 would look like.

## Slide 26: Alt 3 – Collision Modifications
CMF3 from Alt 1 to Alt 3 = 0.835
Apply CMF3 to default collision rate: 134*0.835 =111.89
Insert modified collision rate as a PSV:
Notes: Remember that our calculated CMF for changing the curve from Alt 1 to Alt 3 is 0.835. As shown, we would apply the CMF to collision rate for Alternative 3 and enter it in as a project specific value of 111.89. Collision costs will be left as defaults.

## Slide 27: Alt 3 – Project Segment Definition
Notes: Project segment definition for Alternative 3. All other values will be left as defaults.

## Slide 28: Rehab costs, Alt 3
Notes: Rehab costs for Alt 3: we enter in an overlay cost at years 20, 40, and a reconstruction cost at 60 year.

## Slide 29
19. Enter analysis period
Notes: The analysis timeframe is 80 years. However, the analysis period is used to show what the IRR would be at a specific year. Typically, AT would use 20 years. If the IRR passes 4% at year 20, the alternative would be economically beneficial. Sometimes, if a large cost occurs at a particular year (such as an overlay at year 20), the IRR won’t be able to converge for that particular year, but will occur the year right before and the year right after. This is why 21 years is used here.
For a 21 year analysis period, both Alternatives 2 and 3 have an IRR greater than 4%, which is the minimum required for an alternative to be deemed economically beneficial.
Both Alternatives 2 and 3 break even at year 10, but Alternative 3 has a higher IRR and a lowest discounted total cumulative costs.

## Slide 30
Notes: We can see how benefits are reflected here when we point out that although Alternative 1 has the lowest investment costs, both Alternatives 2 and 3 generate benefits in the form of high cost savings compared to Alternative 1. Alt3 has a higher NPV and BC ratio than Alt2. Alt 3 is the best option.

## Slide 31: E.g. Alt 1-3 User Costs
Texas
California
Notes: This is a comparison of the vehicle operating costs, travel time, collision and emission costs for Alternative 1-3 using both the Texas and California methods. As you can see, travel time, collision and emission costs they are the same. This makes sense, as the differentiation between methods is only be reflected in the calculation of vehicle operating costs. The operating costs are higher with the Texas method. Reminder how earlier we discussed that the Texas method is more accurate to use for this project because it takes into account the vehicle operating cost associated with the varying radius of the curve, whereas the California method would not in this case, basing it solely on the length of the segment instead.
i.e. the California method only takes the slight difference in length between both into account.
If you had used the California analysis method for this situation, you would be underestimating the actual costs.

## Slide 32: Results for California Method
Notes: The analysis timeframe is 80 years. However, the analysis period is used to show what the IRR would be at a specific year. Typically, AT would use 20 years. If the IRR passes 4% at year 20, the alternative would be economically beneficial. Sometimes, if a large cost occurs at a particular year (such as an overlay at year 20), the IRR won’t be able to converge for that particular year, but will occur the year right before and the year right after. This is why 21 years is used here.
For a 21 year analysis period, both Alternatives 2 and 3 have an IRR greater than 4%, which is the minimum required for an alternative to be deemed economically beneficial.
Both Alternatives 2 and 3 break even at year 10, but Alternative 3 has a higher IRR and a lowest discounted total cumulative costs.
This is the results for california method.

## Slide 33
Notes: We can see how benefits are reflected here when we point out that although Alternative 1 has the lowest investment costs, both Alternatives 2 and 3 generate benefits in the form of high cost savings compared to Alternative 1. However, NPV is negative. B/c ratio is below 1.

## Slide 34: Questions?
34