## Slide 1
Module 6: Bridge Project

## Slide 2
As part of the SWAHD widening project, the existing bridge at the Whitemud Drive and AHD interchange will be widened from 2 lanes to 3 lanes on each direction.
Current WAADT=105,000 (2 way traffic), traffic growth rate 2.5%, posted speed 100km/hr, 0 grades for both alternatives, 1 km tangent segment.
Alternative 1: Widening existing bridge by one lane
Alternative 2: Build a separate one-lane bridge
No Alternative 3
GENERAL INFORMATION
Project information
2
Notes: These are the costs associated with paving, both for construction and for maintenance. For ease of use, maintenance costs will be combined with rehab costs into the Rehab costs column in ProjCostsAlt2 tab

## Slide 3: Assume Operating and maintenance cost is similar for Alt1 & Alt2. Difference between Alt 1 & 2 is construction cost and road user cost during construction period. Will the extra spending for a separate bridge be justified?
Question:
3
Notes: Remember that for a 2-lane paved road, the collision rate depends on width and AADT. We are going to have to try different variables a few times.

## Slide 4
Alternative 1:
  Construction assumed to take 3 years
  Speed limit reduced to 60km/hr during construction
  Construction capital cost $5.1 million, engineering cost 10% of construction cost
Alternative 2:
  Construction assumed to take 2 years
  Speed limit maintained to 100km/hr
  Construction capital cost $6.1 million, engineering cost 10% of construction cost
Alternatives
4
Notes: The do minimum option is to leave the gravel road as is, letting the traffic volume naturally grow. The other alternative is to pave the road now.

## Slide 5
1. Go to Project Defn tab.
2. Click in the Vehicle Running Cost to select method: California (Fuel & Non-Fuel Costs), which is default, or Texas (Curvature & Gradient).
Defining your project
5
Notes: Since the curvature and/or gradient does not differ between alternatives, we will choose the California method to calculate vehicle running costs.

## Slide 6
3. Enter a name for your project.
4. Observe the remainder of the tab. Do you have project specific values?
?
6
Notes: Enter in a name for your project. Observe the remainder of the Project Defn tab. Consider whether you have project-specific values available for vehicle occupancy, unit costs for time, and vehicle operating costs. In this case, we do not.

## Slide 7
5. Go to Alt 1 tab.
6. Select Project Type.
7. Select the setting.
8. Choose a name for Alternative 1.
7
Notes: In Alt 1 tab: If you click on the Project Type cell, a drop-down list of possible options appears. In this case we will select Overlay (rehabilitation). Then, select whether the setting is rural or urban by clicking on the cell adjacent to the project type.
Enter in a name for Alternative 1.

## Slide 8
9. Identify the construction start/end years.
10. Enter original (historical) project cost (optional).
8
Notes: Identify the Construction Start/End Years. Enter the Original (Historic) Project Cost. This is optional, and is only applicable if no significant amounts of construction costs are needed with this alternative. Example: for a “do minimum” alternative

## Slide 9
11. Enter construction costs for Alt 1.
12. Enter any specified O&M costs. Leave blank to only use scheduled O&M costs.
9
Notes: Enter the construction costs. For Alternative 1, an overlay cost is required, i.e. a minor construction cost to keep the road in useable condition.
Next, enter Specified Operating and Maintenance costs (if any). Leave blank to only use Scheduled O&M costs, which will be applied by default unless the user selects “Do Not Use” under the Scheduled O&M category under Project Segment Definition inputs. For this example we will be leaving it blank.

## Slide 10
13. Enter PSVs for collision rate and percentage of collision type, if available.
10
Notes: Enter Project Specific Values for Collision rate if any, and percentage of collision type for 6 different road types. We will practice using the charts available in the Collision Rates tab.

## Slide 11
11
14. Define your project segments.
Notes: No Specified Operating and Maintenance costs will be entered. Rather we will input the combined rehab/maintenance costs into the ProjCostsAlt tabs.
We will figure out the collision rates later; first we will finish defining Alt 1 and Alt 2.

## Slide 12
15. Define project segment traffic mix.
16. Define trip purpose by vehicle type.
12
Notes: Edit the Project Segment Traffic Mix and Trip Purpose by Vehicle Type, if there is project specific information different from the default values provided.
Defaults will be used for this example so no change is needed.

## Slide 13
17. Go to ProjCostAlt1 tab.
18. Enter rehab costs under ProjectCostsAlt1 tab.
13

## Slide 14
Repeat Steps 1-18
for Alternative 2

## Slide 15
15

## Slide 16
ALTERNATIVE 2 SCREENSHOTS:
16

## Slide 17
17
Notes: Screenshot of top part of Alt 2.

## Slide 18
18

## Slide 19
Results

## Slide 20
20
19. Enter analysis period

## Slide 21
21

## Slide 22: Questions?
22