## Slide 1
Module 7: Overlay vs. Grade-widening

## Slide 2: Should we
8.0 m
3:1 sideslope
12.4 m
6:1 sideslope
centreline and shoulder rumble strips
OVERLAY
GRADE-WIDEN
OR
?
2
Notes: For example 2, we will evaluate whether we should overlay or grade-widen for a specific project. The existing road is 8 m wide with a 3:1 sideslope. After grade-widening, the road would be 13.4m, with 6:1 sideslopes and rumble strips on both centreline and shoulders.

## Slide 3
Alternative 1: The “do minimum” option, i.e. only do overlay now and grade widen later
Alternative 2: Grade widen now, overlay later
No Alternative 3 in this example.
Alternatives
3
Notes: We will only consider two alternatives. Alternative 1 is to simply continue doing the overlay, considering the likely need to grade widen later. Alternative 2 is to grade widen now, and then overlay as needed in the future.

## Slide 4
2-lane, undivided paved highway in rural setting
4 kilometre length at 1% grade
Posted and running speed is 100 km/h
The road cost $4,000,000 to build originally in 1998.
Overlay cost is estimated at $300,000 / km
Grade-widening cost is estimated at $565,600 / km
Assume engineering costs are 10% of construction costs
No additional land required
AADT is 2,875 and traffic growth rate is 3%, linearly
GENERAL INFORMATION
Project information
4

## Slide 5
1. Go to Project Defn tab.
2. Click in the Vehicle Running Cost to select method: California (Fuel & Non-Fuel Costs), which is default, or Texas (Curvature & Gradient).
Defining your project
5
Notes: Since the curvature and/or gradient does not differ between alternatives, we will choose the California method to calculate vehicle running costs.

## Slide 6
3. Enter a name for your project.
4. Observe the remainder of the tab. Do you have project specific values?
?
6
Notes: Enter in a name for your project. Observe the remainder of the Project Defn tab. Consider whether you have project-specific values available for vehicle occupancy, unit costs for time, and vehicle operating costs. In this case, we do not.

## Slide 7
5. Go to Alt 1 tab.
6. Select Project Type.
7. Select the setting.
8. Choose a name for Alternative 1.
7
Notes: In Alt 1 tab: If you click on the Project Type cell, a drop-down list of possible options appears. In this case we will select Overlay (rehabilitation). Then, select whether the setting is rural or urban by clicking on the cell adjacent to the project type.
Enter in a name for Alternative 1.

## Slide 8
9. Identify the construction start/end years.
10. Enter original (historical) project cost (optional).
8
Notes: Identify the Construction Start/End Years. Enter the Original (Historic) Project Cost. This is optional, and is only applicable if no significant amounts of construction costs are needed with this alternative. Example: for a “do minimum” alternative

## Slide 9
11. Enter construction costs for Alt 1.
12. Enter any specified O&M costs. Leave blank to only use scheduled O&M costs.
9
Notes: Enter the construction costs. For Alternative 1, an overlay cost is required, i.e. a minor construction cost to keep the road in useable condition.
Next, enter Specified Operating and Maintenance costs (if any). Leave blank to only use Scheduled O&M costs, which will be applied by default unless the user selects “Do Not Use” under the Scheduled O&M category under Project Segment Definition inputs. For this example we will be leaving it blank.

## Slide 10
13. Enter PSVs for collision rate and percentage of collision type, if available.
?
If PSV’s are not available, the user can check the graphs / table under the Collision Rates tab.
10
Notes: Enter Project Specific Values for Collision rate if any, and percentage of collision type for 6 different road types. We will practice using the charts available in the Collision Rates tab.

## Slide 11
2008-2012 data
11
Notes: We are looking at a 2 lane paved undivided highway.
Remember that our AADT is 2,875 and our existing roadway width is 8 metres. Therefore, according to the green line on this chart, our collision rate would be estimated at 103.

## Slide 12
Since we were able to obtain a more specific value from the charts, we enter it here:
12
Notes: We enter in our obtained value of 103 in the Project Specific Value cell corresponding to the 2 Lane paved road. This will ensure that 103 is used rather than the default value of 134.3. Make sure it is entered in the rural collision rates section, not the urban.

## Slide 13
14. Define your project segments.
13
Notes: Define your project segments. For this example, it is acceptable to use one segment only as we assume it is a straight, uniform length of roadway. The screenshots show what the columns would look like if you inputted all the information as specified previously.
Due to the age of the surface, we would use the “Paved 2nd” Scheduled Maintenance Cost Category, and input the age of the surface in the last column.

## Slide 14
15. Define project segment traffic mix.
16. Define trip purpose by vehicle type.
14
Notes: Edit the Project Segment Traffic Mix and Trip Purpose by Vehicle Type, if there is project specific information different from the default values provided.
Defaults will be used for this example so no change is needed.

## Slide 15
17. Go to ProjCostAlt1 tab.
18. Enter rehab costs under ProjectCostsAlt1 tab.
15
Notes: Note that since Alternative 1 is referring to the second overlay happening now, we estimate that grade-widening would be required at year 20 to keep the road in an useable condition. Then, overlay costs would be required for years 40 and 60, to ensure accurate costs are accounted for the entire analysis timeframe. Reminder that all costs are entered in today’s dollars.

## Slide 16
Repeat steps 1-18
for Alternative 2

## Slide 17: ALT 2
17
Notes: Alt 2 screenshot

## Slide 18
Collision rate modification (CMF)
A CMF of 0.89 can be applied when the sideslope is flattened from 3:1 to 6:1
Source: CMF Clearinghouse www.cmfclearinghouse.org
18
Notes: During grade-widening, the sideslope will be flattened. In this example, from 3:1 to 6:1. We can estimate a safety benefit associated with this improvement in the form of a lower collision rate. Looking at the Clearinghouse collision modification factors inventory database, two CMFs are applicable as shown in the screenshot. Here we apply the more conservative value of 0.89, as we don’t know the quality of the rating.

## Slide 19
Collision rate modification (CMF)
Source: CMF Clearinghouse www.cmfclearinghouse.org
A CMF of 0.8 can be applied when rumble strips are added to both shoulders and centreline
19
Notes: After grade-widening, rumble strips will be added to both the shoulders and the centreline. Looking at the Clearinghouse collision modification factors inventory database, we can apply a value of 0.8 with a fairly high degree of confidence (as the star quality rating is 5).

## Slide 20
2008-2012 data
20
Notes: Remember that our AADT is 2,875. With a widened road of 12.4 m, we use the lowest blue line to estimate our collision rate at 68. Intuitively we know that it makes sense that the collision rate is lower with a wider roadway. However, there are additional safety benefits to having flatter sideslopes and rumble strips.

## Slide 21
CMF for widening from 8 to 12.4 m (chart): 68/103 = 0.66
CMF for sideslope flattened from 3:1 to 6:1 = 0.89
CMF for adding shoulder and centreline rumble strips = 0.8
Combined CMF = 0.66*0.89*0.8 = 0.470
CMF used in the calculation = 0.6*
New estimated collision rate = 103*0.6 = 61.80
Combining CMF’s
21
Notes: Our new collision rate for the 13.4 m wide road is 68. Remember our collision rate for the 8 m wide road was 103. Using these values, this amounts to a collision modification factor of 68/103 = 0.66
We also have an applicable CMF of 0.89 for a sideslope flattened from 3:1 to 6:1, and a CMF of 0.8 for the installation of shoulder and centreline rumble strips of 0.8.
Therefore, we create a combined CMF of 0.66*0.89*0.8 = 0.470
Use some engineering judgement when applying multiple CMFs. It is possible that collision rate of 68 recorded on all provincial highways of width >11.5m may have many kms with flatten sideslops and rumble strips. Therefore, some of these features are already accounted for. To be more reasonable, it is prudent to use an overall CMF of 0.65 rather than 0.47.
Our new collision rate is 103*0.65 = 66.95

## Slide 22
CMF 0.6 value was chosen based on the combination of CMFs, local Alberta collection data, and engineering judgement.
According to the CMFs, it seems that a 53% reduction is possible. However Alberta data shows 34% has been observed on Alberta highways.
Considering many (but not all) wide highway in Alberta have flattened slope and some ruble strips, an overall reduction of 40% is a reasonable perdition.
Why do we use CMF 0.6?
22
Notes: Our new collision rate for the 13.4 m wide road is 68. Remember our collision rate for the 8 m wide road was 103. Using these values, this amounts to a collision modification factor of 68/103 = 0.66
We also have an applicable CMF of 0.89 for a sideslope flattened from 3:1 to 6:1, and a CMF of 0.8 for the installation of shoulder and centreline rumble strips of 0.8.
Therefore, we create a combined CMF of 0.66*0.89*0.8 = 0.470
Use some engineering judgement when applying multiple CMFs. It is possible that collision rate of 68 recorded on all provincial highways of width >11.5m may have many kms with flatten sideslops and rumble strips. Therefore, some of these features are already accounted for. To be more reasonable, it is prudent to use an overall CMF of 0.65 rather than 0.47.
Our new collision rate is 103*0.65 = 66.95

## Slide 23
23
Notes: We input our new estimated collision rate of 66.95 as a project-specific value under rural 2 lane paved, and leave collision costs as defaults.

## Slide 24
ALTERNATIVE 2 SCREENSHOTS:
24
Notes: Enter in project segment information for Alternative 2. The only difference from Alternative 1 will be the scheduled maintenance category, which will be paved base.
All other values under the Alt2 tab will be left as defaults.

## Slide 25
PROJCOSTSALT2
25
Notes: Under ProjectCostsAlt2 tab, we enter in applicable overlay costs at years 20, 40 to ensure we account for all reasonably foreseeable costs over the analysis period.

## Slide 26
26
19. Enter analysis period
Notes: These are the results for an analysis period of 20 years. The analysis period is the year at which you’d like to view the IRR. AT typically deems a project economically feasible if the IRR is greater than 4% at year 20. The rest of the indicators shown below are calculated over the 80 year timeframe.
For this project, Alternative 2 IRR is very high at 15.9% and the project pays for itself in just 8 years.
Total cumulative costs for Alternative 2 are less than for Alternative 1, as benefits are realized in the form cost savings.

## Slide 27
27
Notes: The investment costs of Alternative 2 are higher than those of Alternative 1. However, there are positive benefits in the forms of cost savings realized with Alternative 2, because the expected collision rate is lower with a wider shoulder, flatter sideslopes, and rumble strips. The benefit cost ratio is 4.3, which means that the benefits significantly exceed the costs for Alternative 2 – this is consistent with the high IRR value. With such results, it would be much more fiscally responsible to grade-widen now as opposed to waiting for 20 years, if you know you will need to grade-widen in 20 years anyway.

## Slide 28
Raise Alt 1 and Alt 2 speed to 110 km/h
Notes: Now let’s do some sensitivity analysis. First, we want to see what the results would be if the running speed for Alt1 and Alt2 will be raised to 110km/h.

## Slide 29
29
19. Enter analysis period
Notes: These are the results for an analysis period of 20 years. The analysis period is the year at which you’d like to view the IRR. AT typically deems a project economically feasible if the IRR is greater than 4% at year 20. The rest of the indicators shown below are calculated over the 80 year timeframe.
For this project, Alternative 2 IRR is very high at 15.9% and the project pays for itself in just 8 years.
Total cumulative costs for Alternative 2 are less than for Alternative 1, as benefits are realized in the form cost savings.

## Slide 30
30
Notes: The investment costs of Alternative 2 are higher than those of Alternative 1. However, there are positive benefits in the forms of cost savings realized with Alternative 2, because the expected collision rate is lower with a wider shoulder, flatter sideslopes, and rumble strips. The benefit cost ratio is 4.3, which means that the benefits significantly exceed the costs for Alternative 2 – this is consistent with the high IRR value. With such results, it would be much more fiscally responsible to grade-widen now as opposed to waiting for 20 years, if you know you will need to grade-widen in 20 years anyway.

## Slide 31
AADT=500
Notes: Then we will see what if the traffic volume is as low as 500.

## Slide 32
Results
32
Notes: Based on these results (and continuing to use a 20 year analysis period), we can see what a difference the lower traffic volume makes. However, the IRR is still greater than 4%, and the project breaks even in 20 years.

## Slide 33
Results cont.
33
Notes: The NPV is still positive, and b/c ratio is still above 1. Alternative 2 is still more economically feasible than Alternative 1, even with a low traffic volume.

## Slide 34: Questions?
34