## Slide 1
Module 8: To Pave or Not to Pave

## Slide 2
Alternative 1: The “do minimum” option, i.e. continue maintaining the gravel road as is.
Alternative 2: Pave gravel road now
No Alternative 3 in this example.
Alternatives
2
Notes: The do minimum option is to leave the gravel road as is, letting the traffic volume naturally grow. The other alternative is to pave the road now.

## Slide 3
A gravel road is 12 years old. Do we pave or keep gravel?
2-lane, 9m wide, undivided gravel highway in rural setting
5 km length at 1% grade, tangent, no curve
Paved road would be 8.5 m wide
Average (running) speed is 80 km/h on gravel; 105 km/h on paved
Traffic growth rate is 3%, linearly
GENERAL INFORMATION
Project information
3
Notes: The gravel road is at the end of its first 12 year cycle and we have to decide whether to pave it or keep as gravel (reshape subgrade and add fresh gravel). The assumptions are listed.

## Slide 4
$14,400 / 2 lane km costs initially, and then every 12 years for re-shaping subgrade. Engineering costs are 10%.
Every year, $ 8,000 / 2 lane km for maintenance and general rehab costs and applying fresh gravel every 3 years on average
GENERAL INFORMATION
Gravel Road Costs
4
Notes: These are the gravel costs, both for construction and for maintenance. For ease of use, we will add maintenance costs with the rehab costs into the Rehab costs column in ProjCostsAlt1 tab

## Slide 5
Grading: $300,000 / 2 lane km
Base/Pave: $344,000 / 2 lane km – includes base/1st stage pave & final stage pave
Engineering costs are 10%
Yearly cost for general maintenance / rehab is: $9,800 / 2 lane km
Overlay every 20 years at $205,000 / km (includes engineering costs)
GENERAL INFORMATION
Paving Costs
5
Notes: These are the costs associated with paving, both for construction and for maintenance. For ease of use, maintenance costs will be combined with rehab costs into the Rehab costs column in ProjCostsAlt2 tab

## Slide 6: At what AADT (and resulting collision rates) does the project become economically feasible?
Question:
6
Notes: Remember that for a 2-lane paved road, the collision rate depends on width and AADT. We are going to have to try different variables a few times.

## Slide 7
1. Go to Project Defn tab.
2. Click in the Vehicle Running Cost to select method: California (Fuel & Non-Fuel Costs), which is default, or Texas (Curvature & Gradient).
Defining your project
7
Notes: Since the curvature and/or gradient does not differ between alternatives, we will choose the California method to calculate vehicle running costs.

## Slide 8
3. Enter a name for your project.
4. Observe the remainder of the tab. Do you have project specific values?
?
8
Notes: Enter in a name for your project. Observe the remainder of the Project Defn tab. Consider whether you have project-specific values available for vehicle occupancy, unit costs for time, and vehicle operating costs. In this case, we do not.

## Slide 9
5. Go to Alt 1 tab.
6. Select Project Type.
7. Select the setting.
8. Choose a name for Alternative 1.
9
Notes: In Alt 1 tab: If you click on the Project Type cell, a drop-down list of possible options appears. In this case we will select Overlay (rehabilitation). Then, select whether the setting is rural or urban by clicking on the cell adjacent to the project type.
Enter in a name for Alternative 1.

## Slide 10
9. Identify the construction start/end years.
10. Enter original (historical) project cost (optional).
10
Notes: Identify the Construction Start/End Years. Enter the Original (Historic) Project Cost. This is optional, and is only applicable if no significant amounts of construction costs are needed with this alternative. Example: for a “do minimum” alternative

## Slide 11
11. Enter construction costs for Alt 1.
12. Enter any specified O&M costs. Leave blank to only use scheduled O&M costs.
11
Notes: Enter the construction costs. For Alternative 1, an overlay cost is required, i.e. a minor construction cost to keep the road in useable condition.
Next, enter Specified Operating and Maintenance costs (if any). Leave blank to only use Scheduled O&M costs, which will be applied by default unless the user selects “Do Not Use” under the Scheduled O&M category under Project Segment Definition inputs. For this example we will be leaving it blank.

## Slide 12
13.We will come back to collision rate and percentage of collision type.
?
12
Notes: No Specified Operating and Maintenance costs will be entered. Rather we will input the combined rehab/maintenance costs into the ProjCostsAlt tabs.
We will figure out the collision rates later; first we will finish defining Alt 1 and Alt 2.

## Slide 13
14 Define your project segment(s)
13
Notes: Define your project segments. For this example, it is acceptable to use one segment only as we assume it is a straight, uniform length of roadway. The screenshots show what the columns would look like if you inputted all the information as specified previously.
We are not going to use the Scheduled Maintenance – rather we will input the combined rehab/maintenance costs into the ProjCostsAlt tabs. Lastly we input the age of the surface in the last column.
We are looking for the AADT that would make paving economical given the site conditions. We will start with a guess of 2000. Next we would define project segment traffic mix and trip purpose if necessary. We are using the defaults so no change is required.

## Slide 14
15. Define project segment traffic mix.
16. Define trip purpose by vehicle type.
14
Notes: Edit the Project Segment Traffic Mix and Trip Purpose by Vehicle Type, if there is project specific information different from the default values provided.
Defaults will be used for this example so no change is needed.

## Slide 15
15
17. Go to ProjCostAlt1 tab.
18. Enter rehab costs under ProjectCostsAlt1 tab.
Notes: Using the rehab/maintenance costs provided in the earlier slides, we enter in the expected costs for the 80 year time frame for Alt 1. We are assuming that the road stays as gravel for this entire time. Therefore, every year will have maintenance/rehab costs for general upkeep and adding fresh gravel every 3 years on average, and every 12 years will be a cost for re-shaping the subgrade.

## Slide 16
Repeat Steps 1-18
For Alternative 2

## Slide 17: ALT 2
17
Notes: Screenshot of top part of Alt 2.

## Slide 18
ALTERNATIVE 2 SCREENSHOTS:
18
Notes: Enter in your project segment definition. The differences here from Alternative 1 are that it is a 2-lane paved surface, and running speed is higher. Make sure you always have the same AADT entered in both alternatives.
All other values will be left as defaults.

## Slide 19
19
Notes: Rehab + maintenance costs for Alt 2, including a yearly upkeep cost and an overlay cost every 20 years.

## Slide 20
Collision Rates

## Slide 21: Selecting a collision rate from chart based on 8.5 m width:
ALTERNATIVE 2 SCREENSHOTS:
2008-2012 data
21
Notes: As Alternative 2 involves a paved road of 8.5 m width, we will use the purple line to select a collision rate based on our AADT. Our first guess of AADT will be 2000, so the resulting collision rate would be about 117.

## Slide 22
Collision rate of gravel road:
149.4/134.3 = 1.11x that of 2 lane paved
22
Notes: From the default value tables, the collision rate of gravel road is 149.4/134.3 = 1.11 times that of 2 lane paved. We need to account for difference in collision severity as well as the rate as shown above.

## Slide 23: Alt 1 Collision Rate PSV
117 * 1.11 = 129.87
23
Notes: Since we know the collision rate for an AADT of 2000 and a width of 8.5m for paved road is 117, we multiply it by the factor of 1.11 determined earlier (of how a gravel road collision rate would correspond to a paved road collision rate).

## Slide 24: CMF for centreline rumble strips
24
design CMF=0.9
Notes: Assuming that centreline rumble strips will be installed on the 2 lane undivided roadway, we can apply a CMF of 0.88 to the collision rate of 117. As some existing paved 2 lane road in Alberta already have center line rumble strips, it is prudent to estimate that the effects will be low. Therefore, we use 0.9 instead of 0.88 to account for this (as most of Alberta’s 2 lane undivided highways currently do not have centreline rumble strips).

## Slide 25: Alt 2 Collision Rate PSV
117 * 0.9 = 105.3
25
Notes: Since we know the collision rate for an AADT of 2000 and a width of 8.5m for paved road is 117, we multiply 117 by the CMF of 0.9 obtained from CMF Clearinghouse and enter the result as a PSV in Alt 2.

## Slide 26: 19. Enter analysis period
26
Notes: These are the results for base year AADT of 2000 and analysis period of 21 years. The analysis period is the year at which you’d like to view the IRR. AT typically deems a project economically feasible if the IRR is greater that 4% at year 20. The rest of the indicators shown below are calculated over the 80 year timeframe. Sometimes, if a large cost occurs at a particular year (such as an overlay at year 20), the IRR won’t be able to converge for that particular year, but will occur the year right before and the year right after. This is why 21 years is used here.
Here the results show that paving (Alternative 2) is economically feasible – the IRR is 12.3% more than 4%, and it breaks even point at year 10.

## Slide 27
27
Notes: Alt 2 is economically feasible, the B/C ratio is 1.817 and the NPV is 3.2 million.

## Slide 28
Work to find the
AADT that paving is not economically feasible

## Slide 29: AADT=1000
29
Notes: There might be some different answers here.
For my analysis, I obtained a final AADT of 960 as the base volume requirement for Alternative 2 to break even in the analysis period of 21 years. The IRR has hit 4.1%, total discounted cumulative costs for Alt 2 are now very slightly lower than Alt 1. NPV is positive.

## Slide 30: AADT=1000
RESULTS, ANALYSIS PERIOD = 25 YEARS:
30
Notes: The NPV has become positive now, and the b/c ratio has reached 1.
Though this is a hypothetical situation and there are other factors that would come into play such as dust and riding comfort factors, and maintenance/rehab costs can be highly variable, it gives a general idea of how keeping some low volume roads paved might not be economical.

## Slide 31: Questions?
31